## Slide 1: New Hampshire BC Screening Practices
Total Resource Cost test: “The TRC test estimates benefits via the present value of energy and non-energy impacts over the life of program measures (numerator) and compares that to the costs, defined as the present value of program cost plus out-of-pockets costs that customers pay for energy efficiency measures (denominator).”
Benefits: Savings (kWh, kW, MMBtu) multiplied by avoided cost values from the 2018 Avoided Energy Supply Components Report (AESC)1
  Avoided costs associated with electricity energy (kWh) and capacity (kW), natural gas, other fossil fuels and wood
  Demand Reduction Induced Price Effect (“DRIPE”) for energy and electric capacity
  Embedded environmental costs for electricity associated with emissions of CO2 and Nox, and non-embedded costs for fossil fuels
  Non-energy impacts (NEIs) (not from AESC): 10% adder (20% low-income) as a conservative proxy for the full value of known NEIs, to help ensure symmetrical treatment of costs and benefits and recognize participant impacts
Costs: Total incremental cost of efficient equipment, relative to baseline equipment.
1The AESC study is undertaken by a competitively procured, independent consultant whose work is supervised by a Study Group comprised of regulators, utility staff and energy efficiency consultants from throughout New England. The final work product serves as the source of most avoided costs for the calculation of energy efficiency program benefits for New England states

## Slide 2
Assessment level: “The NH Utilities strive to ensure each individual program meets a benefit cost ratio of 1.0 or greater, with exceptions for income-eligible, education or start-up programs such as the initial years of a new program. Each sector (Residential and Commercial) is designed to meet a benefit cost ratio of 1.0 or greater.”
Discount rate: “For the 2019 Update, the New Hampshire TRC test uses a nominal discount rate of 4.75 percent (based on June 2018 prime rate) and a general inflation rate of 1.86 percent (as reported by St. Louis Fed Reserve) to estimate future benefits, resulting in a real discount rate of 2.84 percent used for benefit calculations.”
  The value of measures is calculated by taking the net present value of applicable real dollar avoided costs over the lifetime of measures.
Other assumptions: Measure lives, early replacement, net-to-gross, etc.
New Hampshire BC Screening Practices
Notes: Need to update the highlighted sentences